Road lighting design by means of genetic algorithm
Rudolf Bayer
Michal Brejcha
Zuzana Pelánová
Jan Zálešák

---
Project goals
- Road lighting design for lighting situation C1 and lighting class S4
- Meeting requirements of standards:
  - Maintained average horizontal illuminance
  - Minimum maintained illuminance
  - Uniformity – given by maximal illumiance
{bar{ E }}_{ M } >= 5 lx
E_{ min,M } >= 1 lx
{E}_{ max,M }=7.5 lx

---
Input variables
- Dx - distance between pillars
- Dy - sidewalk lamp overlap
- Z - pillar high
- α – lamp tilt
- Single-side vs. two-side lamp placement

---
Situational overview
Dimensions:
total sidewalk length 200 m
sidewalk width 3 m
control area length 80 m
unwanted lighting area width 2 m

---
Used luminaires
- Schréder Atos types A1 – A4, B1 – B4, C1 – C4
- Power consumption 50 W to 150 W
- Designed for pedestrian zones, cycleways, emergency lanes, etc.

---
Optimalization method
- A genetic algorithm has been used using Matlab
- Output data validity has been confirmed by comparison with Dialux output

---
Genetic algorithm settings
- Amount of generations: 60
- Population elements: 200
- Crossover probability: 80 %
- Mutation probability: 5 %
- Parent selection: roulette

---
Fitness function

---
Fitness function curve during optimization

---
Optimization results

---
Conclusions
After a few generations an optimal solution could be found (60 generations).
All GA end results were close to results calculated by DIALux and are satisfactory in terms of the required standards.
The given requirements can be met by multiple solutions. Finding specific solutions can be accomplished by adjusting the fitness function.

---
Thank you for your attention